User Manual

Preface

Thanks for you purchase ZC H. D camera series security products, keep an eye on things when you are away from home .This series products use GSM net work with frequency -850-950/1800-1900 ,It can record many hours of full color XVGA (640*480) video at 30pf with audio onto its support up to 16 GB of flash memory.

Instruction:

Use as defense model:

1   Open the cover of the power switch , insert GSM card and TF card , turn the switch into No

2  Bind the master mobile phone with send command BD888888 to the card number of monitor, it will responds with a message as Administrator Bind Sucessful when the binding is sucessed. ( cancel Super binding: Send command JC888888 to the card number of the phone ,after cancel succeed will receive a message as Cancel Administrator Bind)

3 Set defense: It is for setup the detection of the infrared thermal release induction; it will start photographing automatically and store when someone is detected to have entered.

- Defense outside: Send command BFWS to the card number of the phone, after set up defense succeed will receive message Defense Outside Sucessful, it will starts photographing automatically when someone is detected to have entered and sends the images to the binding user’s phone number by MMS.

There are two model of Defense outside

1)   Save Power Defense Outside: it will starts photographing automatically when someone is detected to have entered and send images to the binding user’s phone number by MMS.

- Slide view Defense Outside. It will starts keep photographing automatically after receive the command and sending images to the binding users phone

2  Defense Inside: Send command BF(Slide view model) or BFS (Save power model)to the card number of the phone ,after defense succeed will receive message as Defense Inside Sucessful, it will start photographing automatically when someone is detected to have entered and save images to the TF card.

1) Slide view Defense Inside: It will starts  keep photographing automatically and save images to the TF card

2) Save power Defense Inside: It will starts photographing automatically only when someone who is detected have entered and save images to the TF card

4   Cancel Defense:  Send command CF to the card number of the phone, after cancel succeed will receive message Cancel Defense Sucessful.

Use as under mobile phone control model

1 Open the cover of the power switch, and insert GSM card and TF memory card, turn the switch into No

2  Bind the master mobile phone with send command BD888888 to the card number of monitor, and responds with a message as Administrator Bind Sucessful when the binding is sucessed.( (cancel Super binding: Send command JC888888 to the card number of the phone ,after cancel succeed will receive a message as Cancel Administrator Bind)

3  send command with mobile phone

- Start video.  Sends message LX to the number of the monitor, it will video immediately after receiving the command and responds a short message for the information of video staring. It will make a video automatically for every two minutes when received the command; when the card is full, it will delete automatically the oldest files and continue to video circularly;

- Photograph: Send command as PZ to the card number, which will require the system to photograph automatically and store, and continue to send MMS to the binding mobile phone number when received photographing command.

Command instructions

- BD888888  (Administrator Bind Sucessful)

- JC888888   (Cancel Administrator Bind)

- BF      （Defense Inside Sucessful）

- BFS    （Defense Inside Sucessful）

- BFW       (Defense Outside Sucessful)

- BFWS          (Defense Outside Sucessful)

- CF         （Cancel Defense Sucessful）

- LX   (Send MMS after  every two minutes Video Record ）

- PZ   (Send images to the master mobile phone with MMS after photographing)

- ZJ138XXXXXXXX  (Add User Sucessful)

- SC138XXXXXXXX ( Delete User Sucessful )

- BJ                (Alarm Open Sucessful)

- JC                (Alarm Close Sucessful)

- MDZ              (Motor Turn Left)

- MDF              (Motor Turn Right)

- YS                (Operation Sucessful)

Indicator light instructions

Flash for1 time             Normal LED light

Flash for 2times             Successful defense

Flash for 3 times                 No signal

Flash for 4 times                No SIM card

Flash for 5 times   Full SD card or no SD card, abnormal card

LED is bright for long time      Sending MMS or processing short message

Specifications:

Ac adapter:100V～ 240V/50Hz( USB: 5.5 ,DC: 500MA)

Working temperature -10℃～ +45℃

Storage temperature-20℃～ +60℃

Working humidity10-90％

Working frequency range EGSM900、 GSM1800、 GSM850、 PCS1900

Working protocols GSM PHASE2/2+ (Including GPRS)

Pictures resolution  VGA（ 1280×960）

Video format 3GP

Video resolution 640＊ 480   30pf

Pixel: 130 ten thousands

Build –in Lithium-ion battery    1200mAh

Standby electric: 1.5-2MA

Turn off current：120MA

Shut down current：120MA

Photo current：80MA

Record current：80MA

Slide view model current：60MA